## Slide 1: Communication Protocol
Real Time System MCTE 4324
Muhammad Faris Bin Nor Fathi 1715743

## Slide 2: Modbus
Transmitting information between electronic devices over serial lines (original version) or via the Ethernet.
Modbus comes in several varieties including Serial RTU, Serial ASCII, TCP/IP and UDP/IP.
Data transactions are based on the master/client requesting data from or writing data to the slave/server
Modbus serial uses RS-232 and RS-485 wiring for collecting data from Modbus slaves.
RS-485 supports as many as 32 nodes without repeaters over the range as far as 1,200 m.
The speed that Modbus typically 9,600-19,200 Baud, but network speeds as fast as 115 kb/s.
Commonly used in process and factory automation.
Has error-detection capabilities such as parity, CRC/LRC and checksums as well as diagnostics from the slave/server or master/client interfaces.
Using security appliances or firewalls specifically designed for Modbus with deep packet inspection, such as those available from Tofino Security.

## Slide 3: Profibus
The cable used has purple outer jacket of RS-485 cabling and used the standard DB9 or M12 connectors.
Have Profibus masters and slaves. The master can be a PLC, PAC, or DCS. And the slaves can be a wide array of devices: drives, motors, IOs, sensors, field devices, robots, actuators,
Profibus has two flavors:
  Profibus Decentralised Peripherals (DP)
  Profibus Process Automation (PA).
Collecting multiple inputs and outputs from the field into a local IO device, and then transferring the data through just one cable to the master.
Operate at speeds of 9600 bit/s to 12 megabits/s
Cables up to 1000 meters

## Slide 4: Profinet
Ethernet based industrial communications protocol.
The physical interface used is RJ-45 Ethernet jack (green color).
Built to withstand the rough environment of a factory.
Operates at 100 megabits/s.
Cables up to 100 meter.
Response time less than 1 millisecond/
Has 3 types of addresses
  IP Address
  Mac Addres
  Device Name

## Slide 5: ControlNet
Provides for critical messaging that does not rely on timing to be executed without interfering with the transport of control and I/O data.
Types of devices that the ControlNet network talks to are PLC , I/O chassis,HMIs, personal computers, drives, and robots.
The topology options for ControlNet are trunkline-dropline, star or tree.
Has a data transfer rate of 5 Mbps.
ControlNet cables are RG-6 coaxial cable types with BNC connectors.
Maximum cable distance for ControlNet cables is 1000 meters.
Can support a maximum number of 99 nodes on the network.
The disadvantages are the cost of hardware can be higher and troubleshooting can be more difficult than other protocols.

## Slide 6: DeviceNet
Communication tool that allows to logically talk between a Programmable Logic Controller and many control devices, such as motors, conveyors, flowmeters, level sensors, etc.
There are five types of DeviceNet cables:
  Thick Round
  Thin Round
  Class 1 Round
  KwikLink Flat
  KwikLink Lite Flat
Distances are measured by two variables:
  Trunkline distance
  Total dropline length
Data rates are 125, 250, or 500 Kilobits per second.
Disadvantages of DeviceNet are limited bandwidth, limited message size, and maximum cable length.

## Slide 7: CAN Protocol
Used in e.g. automotive to allow communication between ECUs (Engine Control Units), sensors, anti-lock braking systems, air conditioners, central door locks, airbags, gear control, engine management systems and so on.
Also used in aerospace applications for in-flight analysis and networking of components such as fuel systems, pumps and more.
Provide speed up to 1Mbps.
Uses of the CAN Protocol:
  The CAN protocol is often used for in-vehicle networking of electronic components.
  It is also used in aerospace applications for in-flight analysis and networking of components such as fuel systems, pumps and more.
  Manufacturers of medical equipment often use CAN for creating an embedded network within medical devices.

## Slide 8: I2C Serial Communication
Allows embedded engineers to connect multiple slave devices with one or more master.
For short-distance communication within two ICs (Integrated Circuits) on the same printer circuit board (PCB).
I2C protocol supports speed up to 3.4 Mbps.
Uses only two wires.
Uses of the I2C Protocol:
  Changes the various color setting, such as hue, on a monitor.
  Controls the LED/LCD displays in cell phones
  Helps switching on /off the power supply of internal components
Advantages of using the I2C protocol:
  Flexibility of using multiple master devices to speed up communication and improve the design functionality
  Chip addressing eliminates the need of CS (Chip Select) Lines
  Supports a robust error handling mechanism with the ACK/NACK feature.

## Slide 9: SPI Protocol
Communicate with each other using master-slave architecture.
The number of master devices is limited to one.
Can deliver up to 10Mbps of speed and is ideal for high speed data communication.
The lack of error-checking mechanism and slave acknowledgment feature are some of the major disadvantages.
SPI is known as four-wire serial bus because it consists of four signals:
  master out slave in (MOSI)
  master in slave out (MISO)
  serial clock (SCK),
  slave select (SS)
Uses of the SPI Protocol:
  Apply for communication with temperature, pressure sensors, and video game controllers
  Interface with LCDs and SD cards
  Communicate with FLASH and EEPROM memory
  Read data from a real time clock.

## Slide 10: USB Protocol
The most common protocol in use.
USB protocol was designed for two specific purposes:
  Communicate with peripheral devices
  Supply power to the connected devices if applicable
Data travels in the form of packets that are composed of 8-bit bytes (or multiples of 8-bit bytes, depending on the supported bitrate), where the Least Significant Bit is transmitted first.
Uses only two wires to for data transfer and are faster than the serial and parallel interface.
USB versions supports different speeds such as 1.5Mbps (USB v1.0), 480 Mbps (USB2.0), 5Gbps (USB v3.0).
Uses of the USB Protocol:
  Connect peripheral devices such as keyboards, mouse, printers, etc. to a computer
  Supply power to the peripheral devices
  Charge accessories such as power banks and devices like cell phones and Bluetooth speakers directly from the power outlet or from computers

## Slide 11: RS-232
Used to connect different peripherals such as Monitors, CNCs etc.
Comes in male and female connectors.
Covers distance up to 15 meters at 9600 bps.
Transmitted digitally by logical 0 and 1 and the logical "1" (MARK) corresponds to a voltage in the range from -3 to -15 V while the logical "0" (SPACE) corresponds to a voltage in the range from +3 to +15 V.
Has 9 pinouts such as TxD, RxD, RTS, CTS, DTR, DSR, DCD, GND.

## Slide 12: RS-485
Most used in the industries and are industry preferred protocol.
Can connect 32 line drivers and 32 receivers in a differential configurations but with the help of additional repeaters and signal amplifiers up to 256 devices.
Speed of operation depends on the length of the line and can reach 10 Mbit/s at 10 meters.
The voltage on the lines is in the range from -7 V to +12 V.